## Slide 1: Cyber Tractor Challenge Virtual Terminal and Lab
ISO11783-6 Tutorial and Lab Activity

## Slide 2: ISO 11783 – Virtual Terminal

## Slide 3: ISO 11786 – comic relief

## Slide 4: Agenda
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 5: Agenda
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 6: Virtual Terminal – What is it?
ISO Definition
A virtual terminal (VT) is an electronic control unit (ECU), consisting of a graphical display and input functions, connected to an ISO 11783 network that provides the capability for an ECU, an implement or a group of implements to interact with an operator. The VT provides the capability to display information and to retrieve data from an operator. An ECU, an implement or a group of implements represented by a Working Set Master acquires storage for objects within the VT and on demand displays this stored information to an operator. In this part of ISO 11783, the term working set will be used for an ECU, an implement or a group of implements either represented by a single ECU or a group of ECUs acting as a working set. Working sets on the network can also acquire the use of input and control keys of the VT to allow the operator to send signals back to the working set.
Notes: What’s a VT? Here’s the ISO definition.
In simpler terms, <CLICK TO ADVANCE>

## Slide 7: Virtual Terminal Defined
A Virtual Terminal (VT) is the device that provides:
the human to machine interface
that enables interaction between the operator and the machine.
A VT is like a web browser in concept. Slightly reversed, the many ECUs/Working Sets(WS) publish to the VT on the ISO 11783 (“ISOBUS”).
Just as with the web browser, the VT does not know what is being presented on the screen, it only knows the rules that govern how that presentation appears.
VT
WS 1
WS 2
WS 3
WS n
…
Notes: It is the human to machine interface to enable interaction between the operator and the machine.

## Slide 8: Virtual Terminal – the Goal
Reuse one display
rather than one or more for each implement.
Additionally
VT Auxiliary Control permits many of the independent switches and knobs to be reused as well.

## Slide 9: Virtual Terminal – the Goal
Also, to try to avoid this…

## Slide 10: Virtual Terminal – the Goal
but now, we see, this …
Notes: How many of you have two screens on your computer?

## Slide 11: Virtual Terminal – the Goal
Notes: What does a VT do? It permits the reuse of human machine interface.

## Slide 12: Historical Review – VTv1
~1998
  Work started on defining VT
  People from many companies were involved
  Leveraged concepts from a less successful LBS standard
2001
  A “version 1” draft of the standard stabilized
  Development was well underway at many companies
2001 Agritechnica
  First VTs on display
Work on the standard did not slow down with these first “prototypes”…

## Slide 13: History – Agritechnica 2001

## Slide 14: Historical Review – VTv1 Results
Successes:
  Transferring a User Interface definition across CAN
  Leveraging
    Either color or black and white graphics
    With or without Touch Screen
  Manufacturer Independent User Interface
    Supports either frugal or high-end display technology
  Multi-manufacturer Participation
  Actual Presentation
    Reasonably accurately represented what was delivered
Demonstrated the need to refine the specification

## Slide 15: Historical Review – VTv2
2004
  Work continued from 2001
    Add capabilities / interactions
    Resolve identified incompatibilities
  ISO11783-6:2004
  Published as an International Standard

## Slide 16: Historical Review – VTv2 Results
Successes:
  Industry Level Success in Customer Hands
    Many companies have produced VTs
    Many companies have produced compatible Implements
Challenges:
  Specification was not “precise” enough for all readers
  Led to some incompatibilities
Demonstrated the need to further refine the specification

## Slide 17: History – Agritechnica 2003

## Slide 18: VT Version 3/4
2006
  Task Force commissioned
  VT Version 3 Features
    Replaces VTv2 Auxiliary Controls
  VT Version 4 Features
    Support Additional Regions (Languages)
    Enhance for Precision Farming
    Clarify (~600) Issues that Led to Incompatibilities
2010
  Combined versions released as one document
  ISO11783-6:2010

## Slide 19: Historical Review – VTv3/4 Results
Successes:
  Industry Level Success in Customer Hands
    Many companies have produced VTs
    Many companies have produced compatible Implements
Challenges:
  Getting to Market Fast Enough (addressing the 600 comments)
  ISO11783-14 starts development
    Requires new capabilities in the VT beyond VTv4
Part 14 requires New Features in VT. The work continued…

## Slide 20: VT Version 5
2010
  Task Force work starts
  Features
    Support for Sequence Control (ISO11783-14)
    Clarify Issues (quite a minor list)
2014
  ISO11783-6:2014
    Ballot approved in January 2014
    ~ 110 comments
Challenges:
  Addressing the comments quickly
  Addressing technical issues
Ballot was a topic for discussion earlier this week at TC23/SC19/WG1 Meeting…

## Slide 21: History – VT Versions
Versions
  SAE J1939:~1988 (Work began)
  ISO11783-6:1998 (VT work began)
  ISO11783-6:2001 (VTv1 – DRAFT)
  ISO11783-6:2004 (VTv2)
  ISO11783-6:2010 (VTv3, VTv4)
  ISO11783-6:2014 (VTv5)
  ISO11783-6:2018 (VT Version 6)
  ISO11783-6:2025 (VT Version 7)

## Slide 22: VT – Manufacturer Interoperable
CNH
JOHN DEERE
AGCO
KVERNELAND

## Slide 23: Lab Action – Monitor Network Traffic
CAN Bus Speeds: 250K and 500K
John Deere – Lab setup

## Slide 24: Lab Action – Find the VT
Find the VT Application
Find its menu of VT Clients
Look at each and Explore

## Slide 25: Lab Action – Find the VT
John Deere – Lab setup

## Slide 26: Agenda
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 27: VT – Some Terminology
Virtual Terminal (definition already shown)
Working Set A Working Set (WS) is an implement, or a group of implements represented by a single ECU or group of ECUs
Virtual Implement A (VI) is another name for a Working Set, or client of a VT. VI is not defined by ISO but appears in this PPT.
Object Pool A collection of objects that completely define the operator interface for a single working set. The complete VT definition will be made up of one or more Object Pools, one for each working set.
VT Objects Smallest object in the Object Pool
Notes: Graphic is from Kverneland implement ECU.

## Slide 28: Virtual Terminal – Overview
Soft Key Mask
Key

## Slide 29: VT – 31 Objects (:2004)
Working Set Object
Data Mask Object
Alarm Mask Object
Container Object
Soft Key Mask & Keys
Input Field Objects
Output Field Objects
Window Mask Object
Key Group Object
Output List
Graphic Context Object
Output Shape Objects
Picture Graphic Object
Variable Objects
Attribute Objects
Pointer Object
Macro Object
Auxiliary Type 1 Objects
Auxiliary Type 2 Objects
Color Map Object
Object Label Reference
External Object *
Animation Object
Notes: Above the line represent the 31 objects from VTv2 (ISO11783-6:2004)
Below the line represent the additional objects from VTv3, v4 (ISO11783-6:2010) and v5 (ISO11783-6:2013?)

## Slide 30: VT – 43 Objects (:2010)
Working Set Object
Data Mask Object
Alarm Mask Object
Container Object
Soft Key Mask & Keys
Input Field Objects
Output Field Objects
Window Mask Object
Key Group Object
Output List
Graphic Context Object
Output Shape Objects
Picture Graphic Object
Variable Objects
Attribute Objects
Pointer Object
Macro Object
Auxiliary Type 1 Objects
Auxiliary Type 2 Objects
Color Map Object
Object Label Reference
Notes: Above the line represent the 31 objects from VTv2 (ISO11783-6:2004)
Below the line represent the additional objects from VTv3, v4 (ISO11783-6:2010) and v5 (ISO11783-6:2013?)

## Slide 31: VT – 45 Objects (:2014)
Working Set Object
Data Mask Object
Alarm Mask Object
Container Object
Soft Key Mask & Keys
Input Field Objects
Output Field Objects
Window Mask Object
Key Group Object
Output List
Graphic Context Object
Output Shape Objects
Picture Graphic Object
Variable Objects
Attribute Objects
Pointer Object
Macro Object
Auxiliary Type 1 Objects
Auxiliary Type 2 Objects
Color Map Object
Object Label Reference
External Object
Animation Object
Notes: Above the line represent the 31 objects from VTv2 (ISO11783-6:2004)
Below the line represent the additional objects from VTv3, v4 (ISO11783-6:2010) and v5 (ISO11783-6:2013?)

## Slide 32: VT – 49 Objects (:2018)
Working Set object
Data Mask object
Alarm Mask object
Container object
Window Mask object
Soft Key Mask object
Key object
Button object
Key Group object
Input Boolean object
Input String object
Input Number object
Input List object
Output String object
Output Number object
Output List object
Output Line object
Output Rectangle object
Output Ellipse object
Output Polygon object
Output Meter object
Output Linear Bar Graph object
Output Arched Bar Graph object
Picture Graphic object
Graphics Context object
Number Variable object
String Variable object
Font Attributes object
Line Attributes object
Fill Attributes object
Input Attributes object
Extended Input Attributes object
Object Pointer object
Object Label Reference List object
External Object Definition object
External Reference NAME object
External Object Pointer object
Animation object
Macro object
Color Map object
Auxiliary Function Type 1 object
Auxiliary Input Type 1 object
Auxiliary Function Type 2 object
Auxiliary Input Type 2 object
Auxiliary Control Designator Type 2 Object Pointer
Color Palette object
Graphic Data object
Working Set Special Controls object

## Slide 33: VT – 28+ Events (for Macros)

## Slide 34: VT – 64+ Commands

## Slide 35: Virtual Terminal – Presentation
Key
Bar Graph
Polygons, Lines, Bitmaps
Ellipse, Bitmaps
Numbers
Text
Notes: Here’s a screen from a sprayer that presents several of the possible elements in the user interface.
The VT protocol was designed based on the limited bandwidth available on CAN. In spite of that, it can do some very amazing things, and can support a very rich presentation and interaction. Even limited animation is possible.
Image courtesy Spraying Systems.

## Slide 36: Agenda
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 37: Developer Perspective
Object Pool Construction
  Ex. Definition of a Data Mask
Authoring Tools
Implantation Into a Controller
Communication with VT

## Slide 38: Object Hierarchy
Parent Object can have 0 to 255 Child Objects
Many Child Objects can be a Parent Object
Objects can be “reused” for efficiency
Data Mask
Container
Container
Circle
Button
Container
Rectangle
Circle
List
Image 1
Image 2
Text Item
Rectangle
Image 1

## Slide 39: Object - Hierarchy
Performance Monitor - Settings
Implement
Status Source
Implement
Width
(ft)
Time Since Last Reset
(h)
Service Interval
(h)
Current Recording
Status
Recording On/Off

## Slide 40: Object Pool Construction
00 10
01
34
34 12
01
00
01 20
40 00
40 00
Object ID
Type – Data Mask
Background Color
Soft key Mask
# Obj to Follow
# Macros to Follow
Obj ID
X Location
Y Location
Macro Event ID
Macro Obj ID
[2]
[1]
[1]
[2]
[1]
[1]
[2]
[2]
[2]
[1]
[1]
Object ID
Type – Line
Line Attributes
Width
Height
Line Direction
# Macros to Follow
Macro Event ID
Macro Obj ID
[2] 01 20
[1] 0D
[2] 02 20
[2] 80 00
[2] 40 00
[1] 00
[1] 00
[1]
[1]
Notes: But how do we define a presentation? This is getting into some deep details.
Each Object is uniquely identifiable. This is necessary for design, and for run-time manipulation. Here, we see a data mask.
We’ll define the color and place another object (a line) on it.
As you see, the Data Mask has references to the Line Object
The Line Object has attributes for drawing the line.
This simple set of relationship can be extended to a pool with 1000’s of objects and interactions.

## Slide 41: Object Pool Construction
Crop
Yield Dry
Yield Wet
Moisture - Field
Flags On
Corn
185
210
12%
1,3
In Object Pool:
Container
Rectangle #101
Rectangle #102
Text #105
Text #…
Text #106
Output Field #233
Output Field #234
Output Field #…
Data Mask

## Slide 42: Authoring a User Interface
01 00 1C 08 00 AD 00 01 15 04 FF FF FF 02 00 1C
08 00 AD 00 01 C3 04 FF FF FF 03 00 1C 08 00 A0
IOP
Notes: So, these things called Object Pools are a bunch of pretty tightly compressed streams of binary. One way to create these things is <Advance>. And eventually, you get <Advance> a pool. But good luck debugging it.
All this stuff gets packed into one or more “files”. The industry has mostly settled on IOP (ISOBUS Object Pool) for the file format. There is no required file format, but from the definition of the pool, this is the natural outcome.

## Slide 43: Authoring Tools
CNH: VT Object Creation
WTK: Mask Generator
Farmix: PoolEdit
OSB: VT Designer
DLG: pConvert
Jetter: ISO-designer
JD: JDGUI-Design
Notes: There are commercial and open-source tool for creating the object pools. Some other companies have their own proprietary version as well.
WTK: Mask Generator – http://www.wtk-elektronik.de/fileadmin/pdf/Prospekt_MaskGenerator_web.pdf
Farmix: PoolEdit – http://autsys.tkk.fi/en/Farmix/PoolEdit
OSB: VT designer – http://vt-designer.com/
DLG: pConvert – originally designed for testing of VTs, was never designed for development purposes.
Jetter: ISO-designer – https://www.jetter.de/en/products/software/iso-designer.html?l=5
CNH: <Proprietary Design Tool> VT Object Creation Tool
JD: <Proprietary Design Tool> JDGUI-Design

## Slide 44: Authoring Tools - JDGUI-Design

## Slide 45: Publishing to a VT
We need an ECU
We need it to host an Object Pool
We need it send the Pool to a VT
We need it to interact with the VT

## Slide 46: Implantation Into a Controller
// Operating Sys.
// Application.c
IOP
Pool to Code
Converter
// myPool.c
char Pool[] =
{
0x12, 0x01, …
0x34, 0x00, …
0x10, 0x80, …
0x30, 0xB3, …
0x0D, 0x8A, …
};
Compiler
Hex File for
Programming
Programming
Tool
Notes: There are many ways, and this shows only one possibility.

## Slide 47
Notes: A bit more detailed and showing other steps in the cycle.
This is the JD work-flow, but it is similar to that of other companies.

## Slide 48: Embedded System - Software
Virtual Terminal
VT Engine
ISO 11783
Protocol Stack
Implement
VI Engine
ISO 11783
Protocol Stack
VT Application
For Presentation
VI Application
For Presentation
IOP
Notes: Conceptually, the VT and the Implement are symmetrical.
Each has an “Application” – [Note the non-ISO term “VI”, which stands for Virtual Implement. So named to be an easy to remember counter-part to the VT]
The VT Application renders the screens and accepts input from the operator
The VI Application provides the business logic to make the implement do what it needs to do
isoAgLib is an “open source” implementation of the software for implements (VIs).

## Slide 49: Example Embedded OS
Power Management
Timing Management
Network Comm
Analog Input
Logic Input
Power Driver
Non-Volatile Memory
Fault Management
Diagnostics
Manufacturer Test
Re-Programming
Specialty I/O Drivers
Task Management
Data Repository
Application
Component 1
Application
Component 2
...
Application
Component N
...
...
...
Extended T.P.
VI Engine
Object Pool
Transport Prot.
File System Driver
UI Logic
Notes: Whether an implement has a full-blown RTOS or not, there are various device drivers (bottom layer).
The yellow boxes are what is “unique” for ISO11783 and Virtual Terminal support.
The Object Pool and Data Masks (visualization), are for the first time separated from the implementation (code).
In support of this is the virtual implement driver, and extended transport protocol, in order to pass this information to the VT.

## Slide 50: VT to VI Communication
VT
VI
VT Status (Here I am)
Get Hardware, … “Great, What can you do?”
Responses… Language: English, Screen: Color 480x480, Softkeys: 10 …
Here’s my Object Pool
Color DataMasks
Color Softkeys
English Text
Detect VT
Query Metrics
Select Resources
Scale Presentation
Change Color
Select Language
Maintain Heartbeat
German Text
French Text
Set Object #24 Value to 123.4
Show DataMask #2
123.4
B&W DataMasks
B&W Softkeys

## Slide 51: VT to VI Communication
VT
VIs
123.4

## Slide 52: Decode an Object Pool
Files on the laptop
racc.log - can log of pool transfer
pool.iop - binary extract
pool.xml - xml decode

## Slide 53: Lab Activity – Find this in the XML
How Many Data Masks in this project? ________
For Data Mask 10360:
  How many child objects? _________
For Data Mask 10103:
  Background color? _________
For Input Number 10310:
  Min and Max value? _________
Notes: 11
4
230
FF, FF, CC
50, 100

## Slide 54: Lab Activity – Live Monitor
Filtering VT to ECU: VT Status PGN: 0E600, VT Function FE
Active Source Address _________
Visible Data Mask ______________

## Slide 55: VT Commands: Keys/Buttons
Byte \ Cmd | Soft Key Activation | Button Activation
1 (VT Func) | 0x00 | 0x01
2 | Key Code | Key Code
3 | Object ID of this Key | Object ID of this Button
4 |  | 
5 | Parent Obj ID | Parent Obj ID
6 |  | 
7 | Key Number | Key Number
8 | 0xFF | 0xFF
Key Code
0 = Released, 1 = Pressed, 2 = Held, 3 = abort
Key Number
User definable num 0 - FF
110 Button Activation

## Slide 56: VT Commands: Keys/Buttons
1CE68026 : 00 40 02 E8 03 01 FF FF
Priority 6, to address 80 from 26
Soft Key, 0x0240, on Data Mask 0x03E8, Press
1CE68026 : 00 40 02 E8 03 00 FF FF
Priority 6, to address 80 from 26
Soft Key, 0x0240, on Data Mask 0x03E8, Release
VT
ECU
VT to ECU
VT to ECU

## Slide 57: VT Command: Control Audio

## Slide 58: Lab Action: Can you make a Beep?
HINT: cansend can0 18E72680#<data>

## Slide 59: Lab Action: Make a Beep - ANSWER
Send this:
18E72680 : A3 02 E8 03 00 01 00 01
Off Time (ms)
On Time (ms)
Freq. (Hz)
2 Beeps
Control Audio

## Slide 60: With a little more effort…
Link to a small symphony

## Slide 61: Agenda
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 62
[Hard] Keys
Data Mask
Soft Key Mask

## Slide 78: Virtual Terminal - Summary
Notes: What does a VT do? It permits the reuse of human machine interface.

## Slide 79: Questions and Answers
Check the Parking Lot for Questions
Open Q & A
Hands-on Lab Next

## Slide 80: More Lab Fun ---
Purpose, History
How it Works
How Implements use it
What do VTs look like
VT Interactions – lab

## Slide 81: A few ECU to VT Commands
Byte \ Cmd | Change Numeric Value | Change Attribute
1 (VT Func) | 0xA8 | 0xAF
2 | Obj ID of Obj to change | Obj ID of Obj to change
3 |  | 
4 | 0xFF | AID of Attr
5 | New Value | New Value
6 |  | 
7 |  | 
8 |  | 
Key Code
0 = Released, 1 = Pressed, 2 = Held, 3 = abort
Key Number
User definable num 0 - FF

## Slide 82: VT Commands: Change Num Val
18E72680 : A8 37 04 FF 78 56 01 00
Priority 6, ECU to VT, to address 26 from 80
Change Numeric Value,
of Object 0x0437,
to 0x00015678
18E68026 : A8 37 04 00 78 56 01 00
Priority 6, VT to ECU, to address 80 from 26
Change Numeric Value Response,
of Object 0x0437, no errors,
to value 0x00015678
ECU
VT
ECU to VT
VT to ECU

## Slide 83: Input Number Obj – Attributes

## Slide 84: Input Number Obj – Attributes

## Slide 85: VT Command Summary

## Slide 86: VT Command Summary

## Slide 87: VT Command Summary

## Slide 88
And that was
the tip
of the Iceberg

## Slide 89: On the laptop
CTC Virtual Terminal and Lab.pptx
  This presentation
racc.log
  CAN log of the ECU and VT
pool.xml
  Extract of the Pool transfer from the log
VT Command Map.xlsx
  Handy resource (see next slide)

## Slide 90: VT Command Map.xlsx
18E72680 : A8 37 04 FF 78 56 01 00
ECU
VT
ECU to VT

## Slide 91: Cyber Tractor Challenge
Can you change something on the screen?
  Value, Text, Color, Location, Data Mask, or more…
Can you spoof the ECU and send it a command?
  Causing it to update the VT to confirm your command…

## Slide 92: Lab Action (Bonus time)
Monitor the network, filtering for:
  ECU to VT (PGN: 0xE700)
    To VT Addr from ECU Addr
    Identifier: 0x1CE72680
  VT to ECU (PGN: 0xE600)
    To ECU Addr from VT Addr
    To Global Addr from VT Addr
    Identifier: 0x1CE68026
  Request Language (PGN: 0xEA00)
    To VT Addr from ECU Addr, To Global Addr
    Identifier: 0x0CEA2680:09FE09, 0x18EAFF80:09FE09
  Language (PGN: 0xFE09)
    From Addr (of the) VT
    Identifier: 0x18FE0926
  Transport Protocol (PGNs: 0xEC00, 0xEB00)
  Extended TP (PGNs: 0xC800, 0xC700)

## Slide 93: Lab Action (Bonus time)
Delete Stored Pools in Gen4
  From w/in the VT Application
Turn off / unplug the Implement ECU
Start a CAN monitor
Turn on ECU
Observe CAN
  Interact with the App